## Slide 1
Yunqi Shi, Ke Xue, Lei Song, and Chao Qian*
School of Artificial Intelligence
Nanjing University, China
Advances in Neural Information Processing Systems 36 (NeurIPS'23)
Macro Placement by Wire-Mask-Guided Black-Box Optimization

## Slide 2
Why we are the best?
The problem we solve
The baselines we beat
The contributions to community
Macro Placement
A vital stage in chip design
Significant improvement
(e.g., 80% wirelength improvement over [Google, Nature’21])
Bring EAs back to the state-of-the-art for macro placement
Reaffirm the potential of EAs for chip design
human experts
TCAD, DAC best paper

## Slide 3
Chip design
Apple A17 Pro
Design Document
Netlist
Chip layout
Wafer
Logic Synthesis
Place & Route
Testing &
Verification
Packaging
Register transfer level (RTL)
RTL Design
What we study
Macro placement: The first step
in place & route, which significantly influences the subsequent stages
Some figures are from [Bei Yu, EDA for AI Chip Designs]

## Slide 4
Macro placement
Sum of the half perimeter of nets’ bounding boxes
Minimization objective: Half Perimeter Wire Length
Non-differentiable!
High-dimensional: Thousands of macros
Constraint:
No-overlapping
Netlist
Chip canvas
To-place macros
Placement result
Power
Timing
Performance:
Congestion
Some figures are from [Jens Vygen, Combinatorial Optimization and Applications in VLSI Design]

## Slide 5
Macro placement
Human experts spend weeks for macro placement, owing to the very large number of macros to be placed and their complex connections
Netlist
Chip canvas
To-place macros
Placement result
Power
Timing
Performance:
Congestion
Design efficient algorithms producing better placement than human experts

## Slide 6
Previous methods
Classical EAs
1980s-2000s
Packing-based solution representation
Optimize by Evolutionary Algorithms (EAs)
[Google, Nature’21]
complexity for mapping
Final performance heavily relies on the initial placement
Low-efficiency and low-scalability
[Murata et al., TCAD’96]
“... it is very slow and difficult to parallelize, thereby failing to scale to the increasingly large and complex circuits of the 1990s and beyond.”
: number of macros

## Slide 7
Previous methods
Analytical Placers
2000s-Now
Smooth the HPWL formulation
Optimize by gradient descent
Overlapping
Get stuck in local optima
Classical EAs
1980s-2000s
Some figures are from [Yibo Lin, DREAMPlace]

## Slide 8
Previous methods
Analytical Placers
2000s-Now
Reinforcement Learning Methods
2021-Now
[Google, Nature’21]
Markov Decision Process
Long training time
Poor exploration
Classical EAs
1980s-2000s

## Slide 9
Previous methods
Analytical Placers
2000s-Now
Reinforcement Learning Methods
2021-Now
We propose a genotype-phenotype mapping inspired by RL formulation
Bring EAs back to the state-of-the-art!
[Google, Nature’21]
Classical EAs
1980s-2000s

## Slide 10
Proposed genotype-phenotype mapping

## Slide 11
Proposed genotype-phenotype mapping
Partition the chip canvas into discrete grids

## Slide 12
Proposed genotype-phenotype mapping
The first macro to place

## Slide 13
The input netlist indicates connection relationships
Proposed genotype-phenotype mapping

## Slide 14
Proposed genotype-phenotype mapping
Invalid location resulting in overlap or exceeding the boundary
Wirelength increment if placing at this grid
Underlined number means the minimum increment
6
6
Calculate the wirelength increment after placing the macro:

## Slide 15
Refer to its original location
Proposed genotype-phenotype mapping

## Slide 16
Proposed genotype-phenotype mapping
Refer to its original location

## Slide 17
Choose the nearest best grid
Place the macro
Proposed genotype-phenotype mapping

## Slide 18
The second macro to place
Proposed genotype-phenotype mapping

## Slide 19
Calculate the wirelength increment after placing the macro at each grid
Proposed genotype-phenotype mapping

## Slide 20
Refer to its original location
Proposed genotype-phenotype mapping

## Slide 21
Proposed genotype-phenotype mapping
Choose the nearest best grid
Place the macro

## Slide 22
Obtain the valid phenotype placement result
Place macro C similarly
Proposed genotype-phenotype mapping
A greedy mapping based on the increment of wirelength
Any placement
Good valid placement
Improve the efficiency

## Slide 23
Optimization based on proposed mapping
Genotype
Evolutionary Algorithm
Phenotype
Initialization: Randomly generate 100 genotype solutions and pick the best
Mutation: Randomly exchange two macros’ locations
Already performs well!
(1+1)-EA

## Slide 24
Genotype
Any black-box optimization algorithm
Phenotype
Optimization based on proposed mapping
(1+1)-EA
Bayesian optimization
Random search

## Slide 25
Comparison with previous SOTA methods
Classical EA method
Analytical
RL
Our methods
WireMask-EA (our proposed framework equipped with EA) achieves the best average rank, and reduces wirelength by 80% compared to [Google, Nature’21]
Table 1: Wirelength (×) obtained by ten compared methods on seven popular ISPD contest chips.
[Google, Nature’21]
Graph [Nature’21]: RL method proposed by Google
DREAMPlace [DAC’19, TCAD’21 Best Paper] : One of the most popular analytical methods
DeepPR [NeurIPS’21] and MaskPlace [NeurIPS’22] : Two recent advanced RL methods
Some important baselines

## Slide 26
Table 2: Wirelength (×) Compared with ChiPFormer on ten popular ISPD and ICCAD contest chips.
Comparison with the latest method ChiPFormer
WireMask-EA outperforms ChiPFormer [Lai et al., ICML’23] on 9 out of 10 chips,
using the same number of evaluations
[Lai et al., ICML’23]

## Slide 27
Comparison with expert-crafted results
Experiments on private industry chip cases:
ChiPFormer outperforms human experts (who place the macros with the help of commercial tool Candence Innovus)
[Lai et al., ICML’23]
WireMask-EA ChiPFormer Human expert

## Slide 28
Visualization by commercial tool Cadence Innovus
Our proposed framework equipped with EA
Most popular
analytical placer
DAC’19 Best Paper
TCAD’21 Best Paper
Our results have much fewer red points, showing better routability and performance
DREAMPlace
Red points in the figure represent congestion points that can’t be routed
WireMask-EA

## Slide 29
Why we are the best?
The problem we solve
The baselines we beat
The contributions to community
Macro Placement
A vital stage in chip design
Significant improvement
(e.g., 80% wirelength improvement over [Google, Nature’21])
Bring EAs back to the state-of-the-art for macro placement
Reaffirm the potential of EAs for chip design
human experts
TCAD, DAC best paper

## Slide 30
We have inspired a recent RL method
[Geng et al., ICML’24]
Inspired by our work, EfficientPlace chooses the action from the feasible grids with minimum wirelength increment, originated from our genotype-phenotype mapping, enhancing RL searching

## Slide 31
Why we are the best?
The problem we solve
The baselines we beat
The contributions to community
Macro Placement
A vital stage in chip design
Significant improvement
(e.g., 80% wirelength improvement over [Google, Nature’21])
Bring EAs back to the state-of-the-art for macro placement
Reaffirm the potential of EAs for chip design
We are working on
Benchmark chip design cases as real-world problems for EAs
Thanks for listening!
human experts
TCAD, DAC best paper